## Slide 1
This presentation is based on content presented at the 2017 Emergency Management information session in November 2017.
Department of Mines, Industry Regulation and Safety(DMIRS) supports and encourages reuse of its information (including data), and endorses use of the Australian Governments Open Access and Licensing Framework (AusGOAL)
This material is licensed under Creative Commons Attribution 4.0 licence. We request that you observe and retain any copyright or related notices that may accompany this material as part of attribution. This is a requirement of Creative Commons Licences.
Please give attribution to Department of Mines, Industry Regulation and Safety, 2018.
For resources, information or clarification, please contact: SafetyComms@dmirs.wa.gov.au or visit www.dmirs.wa.gov.au/ResourcesSafety
Please read this before using presentation

## Slide 4
In the last 5 years, how many people in the room have been involved with structural firefighting either through
training or real incidents? E.g. haul truck or digger fire, donger fire, vehicle fires

## Slide 5: Historical photos

## Slide 6
Generally speaking
Emergency Services personnel are very good at managing the acute risks at incidents.
E.g. Fire, exposures
What we are not so good at, is managing the chronic risks at incidents.
E.g. Long term health impacts from exposure to atmospheric contaminants.

## Slide 7: Background – Toxic Twins
Firefighters think of carbon monoxide (CO) as the silent killer.
Research is pointing to hydrogen cyanide (HCN), as a second and equally hazardous threat to responders with symptoms similar to carbon monoxide poisoning. That is less recognized - acute cyanide poisoning.
HCN is 35 times more toxic than CO, according to researchers.
It can enter the body by absorption, inhalation or ingestion, and its main targets are the heart and brain, where it degenerates the outer tissues to a point where they will never regenerate again.
Hydrogen Cyanide is a bi-product of combustion from ordinary materials of everyday life (insulation, carpets, clothing and synthetics). But the real offender is from combustion of man-made plastic and resins containing combinations of hydrogen, carbon and nitrogen, especially if the fire is hot and in an enclosed space

## Slide 8: Rio Tinto

## Slide 10: Level 2 Structural garments
Nano-Flex Flash hood
Latest technology – revolutionary material
Acts as a filter to reduce exposure
Particle barrier filtration
Thermal and flashover protection
Before
Nano-flex
After
Latest technology
Moisture barrier protection
Light weight and flexible
Level 3 glove
  Level 3 protection
  Superior cut resistance
  Moisture barrier protection
Level 3 structural boot
  Latest technology
  Superior barrier protection
  Superior thermal protection

## Slide 11: level 1 Jacket
Latest technology
Light weight, comfortable and flexible
Personal issue
Proban free

## Slide 12
DOT-System (bag) is a storage device for contaminated protective clothing. Is an encapsulation system developed for emergency services personnel - Reducing exposure from contaminated SCBA and other material during handling and transport - The product also contains a protective compartment for storage of disposable coveralls to change into. - Is easy to work with, safe and specially adapted for fire and rescue vehicles - Can be cleaned in the washing machine (40oC) and re-used. The bag will also be utilised to ship contaminated garments and equipment to the OEM for decon or repair.

## Slide 14
Play Video now https://youtu.be/8IqUKTVWN2E

## Slide 15
Continuous gas monitoring of fresh air base
Specifically testing for CO and HCN (Toxic twins)
Identify any possible contaminates and particles from PPC before dressing down.

## Slide 18
On scene Decontamination
Continuous gas monitoring
Doff SCBA and don P2 mask
Don nitrile gloves
Bag PPE and contaminated gear
Stow in lockers not cab
Return to station
Carry out personal clean
Carry out personal clean
Clean equipment

## Slide 19
2 stage wash
Arrive on station – truck cab clean Don gloves and P2
Wash BARRIO garments
Allow garments to dry, avoid UV. Turn inside out to expedite drying process
Log use & reinstate kit
Shower within 1 hour
SCBA lockers let open to allow for drying
Wipe down surfaces in cab, Including seats, seatbelts, door Trim and foot well

## Slide 20
It is recommended that all offsite decontamination of Rio Tinto PPE is managed by the OEM. All locations should follow the OEMs procedures including the use of the correct transportation packaging.
Isolate the contaminated item from the non-contaminated.
Do not shake or dislodge any particles from the items.
Pack the contaminated item/s in the yellow contamination bags available that are held at the Rio Tinto Location.
Complete and follow the instructions on the Services Request Form

## Slide 21
The OEM are to manage all repairs. This ensures that all repairs will remain Australian Standard compliant.
All garments for repair must first be laundered. The garments must be returned in the bags supplied by the OEM. Always complete the form with all of the required information.
Utilise PPE Service Request Form.

## Slide 22
A log book for each site will be maintained ensuring that each garment is closely monitored.
This will also include the wearer and reason
for laundering.

## Slide 23: Maintain clean environment
Post fire cleaning
Weekly cleaning – post training / pre-handover
Don gloves and P2
Safely park up truck
Sweep floor
Utilise wipes on surfaces
Wash exterior of truck

## Slide 25
PPE posters are available
To be placed in PPE storage locations, training rooms