# Seismic event and/or fall of ground (FOG) occurrence

This template will assist operations preparing to submit an occurrence report on the Safety Regulation System (SRS).

| TIME, LOCATION AND EXTENT OF FOG / DAMAGED ROCKMASS / DAMAGED SUPPORT |
| --- |
| Time and extent | Time of FOG? | FOG tonnes (t) | Damaged area – depth (m) | Damaged area – width (m) | Damaged area - length (m) |
|  | DD/MM/YY HH:MM AM/PM | <numeric> | <numeric> | < numeric> | < numeric> |
| Depth (m below surface) | Mine (deepest active stopes) | At fall of ground (FOG) |
|  | <text description> | <text description> |
| Location of damage site <Attach screen dump from mine software showing development, stopes and major structures> | Lode/block name | Northing | Easting |
|  | <text description> | <text description> | <text description> |
| EXCAVATION DESIGN (For damaged development / accessway) |
| Excavation details – in area of FOG / damage | Date mined | Development width/span (m) | Development height (m) | Perimeter blasting used? |
|  | DD/MM/YY | <numeric> | <numeric> | Yes No |
| SUMMARY DESCRIPTION OF FOG/ DAMAGED ROCKMASS |
| Damage site description | <text description> E.g. stope brow |
| Site geology, structures, stress conditions, presence of water (l/s) <describe> | <text description> E.g. porphyry dyke contact with ultramafics, high stress at brow, dry. |
| Kaiser Rock Damage Scale (see Table 1) (tick one only) | R0 (no rockmass damage) | R1 (minor new fractures) | R2 (minor damage <<1t displaced) | R3 (<1 t displaced) | R4 (1-10 t displaced) | R5 (>10 t displaced) |
| Failure mode (tick correct box) | Static | Seismic (Ref: ACG Generic SRMP) |
|  | Wedge Sliding block Toppling Unravelling | Strain burst (including bulking) | Buckling | Face crush/ pillar burst | Shear rupture/ fault slip | Shakedown |
| SEISMICITY (fill in this section only if a seismic event has occurred) |
| Source mechanism (e.g. high S:P = fault slip) | <text description> E.g. ‘Jog Fault’ slip, observed displacement / heave of 300 mm |
| Seismic event hypocentre | Time of event | Level / RL/ mBS | Northing | Easting | Distance from damage site(s)? |
|  | DD/MM/YY HH:MM AM/PM | <numeric> | <numeric> | <numeric> | <numeric> |
| Magnitude | Seismic system | Local (ML) (ESG) | Richter equivalent (MR) (ISS) | S:P energy ratio |
|  | ISS / ESG / other | <numeric> | <numeric> | <numeric> |
| BLASTING (provide details of last blast before the FOG/seismic event) |
| Most recent blast details | Time of blast | Blast tonnes | Blast type (stope production/ development/other?) | Exclusion zone details (part of mine closed) | Re-entry period – hours after blast (based on Omori Chart analyses) |
|  | DD/MM/YY HH:MM AM/PM | <numeric> | Prod / Dev / Other | <text description> | <Hours> |

| SUPPORT DAMAGE RATING IN FOG/ DAMAGED AREA |
| --- |
| Kaiser Support Damage Rating (see Table 2) (tick one only) | S0 (no damage) | S1 (1st signs of distress) | S2 (loaded, plates deformed, mesh bagged but OK) | S3 (heavy loaded, few broken, mesh bagged, some torn/open) | S4 (major damage, many broken bolts, mesh failed or bagged to capacity, rock ejected between bolts) | S5 (complete failure of support components) |
|  | SC0 (no damage) | SC1 (1st cracks in shotcrete) | SC2 (shotcrete cracked and loaded) | SC3 (shotcrete fractured, debonding, some fragments) | SC4 (shotcrete heavily fractured, large pieces fallen) | SC5 (shotcrete non-functional) |
| INSTALLED GROUND SUPPORT IN FOG/DAMAGED AREA |  |
| Order of installation | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| Support type <bolt / reinforcement name> |  |  |  |  |  |  |  |  |
| Black / galvanised? |  |  |  |  |  |  |  |  |
| Bolt length (m) |  |  |  |  |  |  |  |  |
| Pattern (burden x spacing, m) |  |  |  |  |  |  |  |  |
| Bolt load capacity (t) |  |  |  |  |  |  |  |  |
| Bolt energy capacity (kJ/bolt) |  |  |  |  |  |  |  |  |
| Displacement limit (mm) |  |  |  |  |  |  |  |  |
| Age of support (months) |  |  |  |  |  |  |  |  |
| Condition / corrosion? |  |  |  |  |  |  |  |  |
| Mesh | Sheet size (W x L, m) | Aperture (mm) | Gauge (mm) | Energy (kJ/m2) | Overlap pinned? | Coverage |
|  | <W x L> | <numeric> | <numeric> | <numeric> | Yes No | Backs / Shoulder / Grade line |
| Shotcrete / fibrecrete | Design thickness (mm) | Actual thickness (mm) | Energy (kJ/m2) | Fibre dosage (kg/m3) | UCS (MPa) | Coverage |
|  | <numeric> | <numeric> | <numeric> | <numeric> | <numeric> | Backs / Shoulder / Grade line |
| GENERAL COMMENTS AND REMEDIAL ACTIONS |
| Provide further relevant information. Describe immediate rectifications and actions as a result of this event. Please attach relevant photos, investigation memos, seismic history and data analyses. |

# Table 1	Rock Damage Scale

Reference: Kaiser, P.K., Tannant, D.D., McCreath, D. R. and Jesenak, P.,1992, Rockburst damage assessment procedure; in Rock Support in Underground Mining and Construction, Kaiser and McCreath (eds), Balkema, Rotterdam, pp. 639-647.

# Table 2	Support Damage Scale

Reference: Kaiser, P.K., Tannant, D.D., McCreath, D. R. and Jesenak, P., 1992, Rockburst damage assessment procedure; in Rock Support in Underground Mining and Construction, Kaiser and McCreath (eds), Balkema, Rotterdam, pp. 639-647.